xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec
 xspec							          xspec
 xspec    Spectral data format for XSPEC series of programs.      xspec
 xspec								  xspec
 xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec

    Data files contain the number of observed counts in a PHA channel
(and therefore often use the .PHA extension for the file). Other
information in the file allow for background subtraction and the proper
calculation of effective area and counting statistics to calculate the
source counts cm**-2 sec**-1 and the associated statistical error. The
file is organized as a 'standard format' (SF) binary file (read using
fortran unformatted reads and writes), see the associated documentation
on SF for details. The first records are the SF (standard file) ID
record, and an optional set of history records.  All pha files have SF
identifications of 'xspec data  '. The length of each history record is
included as the first four bytes of the record. Use the OPNRSF
subroutine to open the file for read purposes, and find the number of
history records (see the SF documentation). 

    SF files are organized as packages of records.  The order of the
packages in PHA files is fixed, although some packages are optional and
as far as XSPEC is concerned any other packages may be inserted at
particular points without any real harm.  The packages that XSPEC is
interested in seeing are: 
    'source info ' - Information about the source (not needed by XSPEC,
		     and therefore optional)
    'selectors   ' - Selection criteria used in creating this file (not
		     needed by XSPEC)
    'ass. files  ' - Associated files package
    'file info   ' - Information needed to describe the file (e.g.
		     the no. of channels, etc.)
    'grouping    ' - A grouping card (for grouped data) (optional)
Following this there could be one of three sets of packages depending on
how the data is to be represented: 'pha data' for data in the format of
the actual counts in the observation; 'pha per sec' for data with the
count rate (dividing by the integration time has already been done); and
'pha per cm2s' for the area corrected count rate (divided by area and
time) N.B. that BACKGROUND data ususally has no effective area and thus
should not be represented in the 'pha per cm2s' mode.  Poisson errors
are used for the 'pha data' based packages. For data from the other two
packages there is a required additional package: 'pha errors' which are
in the same units as the pha data (i.e. counts per second or counts per 
cmsquared second). Thus the possible combinations are:
	'pha data    ' - The actual observed counts
		OR
	'pha per sec' followed by
	'pha errors'
		OR
	'pha per cm2s' followed by
	'pha errors'
In addition, for all three cases there could be a package
	'systematics ' - A systematic error to be added (optional).
Following the data there could be optional packages describing detector
specific configuration informtion, that in particular could be useful
for the construction of a response file. Any additional packages must
have different package names.  They may be inserted in any particular
order, but the above packages must be included in the order given.  No
insertions are allowed between the 'file info' package and the various
'pha...' data packages, other than the 'grouping' package. 

    The 'source info' package contains a header record of 72 bytes:
	EPOCH	r8	Observation epoc (all times are in reference
			to this date) (units? MJD? Jul Sec? year/day?)
	START	r8	Observation start time (secs)
	STOP	r8	Observation stop time (secs)
	SYSTEM	i4	Coordinate system flag, should be 0 to indicate
			1950 RA and DEC.
	VECT	r8(3)	Vector triple representing position of source
	NAME	c20	Source Name.

    The 'selectors' package is described in the SELECTORS.DOC file.

    The 'ass. files' package has no information on its header, but
consists of three subsidiary records.  Each is a file name.  XSPEC
requires that these file names be at most 72 characters.  The first file
is a PHA file that is used as the default background file.  If it is all
blanks (at least one character long), or the string "none" or "NONE",
then no background subtraction is performed. 

The second record is the file name of the default detector response file
(see documentation in RESPONSE.DOC). 

The third subsidiary record is a PHA file used to make corrections.  An
example would be the `difference spectra' for the EXOSAT ME detectors. 
The corrections do not contribute to the calculation of the measurement
error (unlike the background file information). 

These records are simple character strings, and should not be delimited
by quotation marks. 

    The 'file info'  package has no subsidiary record.  The package
header buffer contains 100 bytes (only 36 of which are currently used by
XSPEC).  The lay out of the buffer is
    DETID    C16    A character string that uniquely identifies the
		    detector.  This string is not used by XSPEC other than
		    to confirm that the data, background, and response
		    files all come from the same detector.  Of course,
		    other routines that manipulate PHA files may use this.
    NBIN     I4	    The number of data channels in this PHA file (after
		    any data grouping).
    NCHAN    I4	    The number of unbinned data channels.  If NCHAN
		    and NBIN are NOT equal, then XSPEC will look for a
		    grouping package to describe the difference.
    T        R4	    The active integration time (seconds).
    A        R4	    The effective area of the source (cm**2).  This does
		    not include any spectrally dependent area variations,
		    such as telescope vignetting, which are subsumed under
		    the response matrix.
    DEL	     R4	    A background scaleing factor, e.g. the no. of pixels
		    covered in the observation for imaging measurements.
		    This number is used in the background subtraction
		    process.  It has no units.
    COR      R4	    The correction file scaleing factor.  Should be zero
		    if there is no correction file.  It has no units.
    INDICES  R4(3)  A reserved area, not currently used.  Should be zero.
    SPARE    48	    These values should currently all be set to zero.

    The next package contains 'grouping' information for those cases
where the data from channels are not included or adjacent channels are
grouped together. If NCHAN and NBIN are the same, then all the data is
included, ungrouped, and the package is skipped over (and may, in fact,
be totally absent). If NCHAN is less than NBIN, then the package
buffer consists of NBIN bytes, read as a long character string.  If
the ith character is any other character, particularly ' ', or '.', then
that particular channel is not included.  The beginning channel is
indicated by a '+' and trailing members of ac group are indicated by a
'-'.  For example, in a file with 9 unbinned channels, a record like 
 +++-+-+
123456789
indicates 5 binned channels, those being channels 2,3,4-5, 6-7, and 8.

    'pha data', has a buffer of NCHAN R*4s, containing the total number
counts in that channel.  When XSPEC performs fits, it converts the count
rates to background subtracted counts per square cm per second.  See
discussion below for the detailed algorithm.  If package is 'pha per
sec' or 'pha per cm2s' the format is the same, but the units of the data
differ.  A similar format for the 'pha error' package would contain the
error values (r.m.s., not variances) for the 'pha per sec' or 'pha per
cm2s' input data. 

    The 'systematics' package has a buffer of NCHAN R*4s, containing a
fraction, F, used to calculate an estimate  of the fractional SYSTEMATIC
error.  If R is the observed rate (before background subtraction),
OLDERR is the error calculated from poisson statistics ('pha data'
package) or directly input ('pha error' package), and F is the
fractional systematic error, then the estimated total error is 
	ERR = SQRT(OLDERR + (F*R)**2) .
The first N term is from strict Poisson error or from the 'pha error' 
package. If you wish to have no systematic error for the channel, F should 
be zero.

    In some cases there may be a package describing detector specific
information to be used by, for example, response file creation programs. 
These are described in other documentation.


    Background data files and background removal:

Background files have exactly the same format as source data files, i.e.
are SF 'xspec data' files.  If the data file is grouped, then the
background file MUST be grouped the same way, OR, it must be totally
ungrouped (current release of XSPEC). 

If ND, TD, AD, DELD are the values for N, T, A, and DEL from the data
file, and if NB, TB, and DELB are from the background file (AB is not
needed), then the observed rate of counts cm**-2 sec**-1 used in the
fitting analysis is 
	ROBS = ( (ND/TD) - (DELD/DELB)*(NB/TB) ) / AB .
Note that the ratio DELD/DELB allows the number of pixels used in
accumulating the background data to be different then the number used in
accumulating the source data.  For some experiments (e.g. GSPC) both
DELD and DELB will be unity.  For files that contain 'pha per sec' or
'pha per cm2s' packages, then ND/TD, etc. may be found directly.