xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec
 xspec								  xspec
 xspec		Detector response: Format for XSPEC		  xspec
 xspec								  xspec
 xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec

		******Philosophical issues****** 

    How do we define the detector spectral response? All detectors have
spectral information defined by channels. Even detectors with no
spectral resolution (e.g. the Einstein Observatory HRI) can be thought
as a single channel detector. Detected counts are apportioned among the
channels, based on the incident photons energy. However, the
correspondence is not exact, so that a given energy photon has a
probability of being counted in one of several channels. 

    The incident photon spectrum is divided up into energy ranges. The ith
energy range runs from E(i-1) to E(i), in keV. The response "matrix" is 
defined by the values R(j,i) = to the average PROBABILITY that an incident 
photon in the ith energy range will be detected in the jth channel. By 
this definition, the response does not include any detector area term. The
actual values of the energy ranges, the E(i), are chosen by the generator 
of the response matrix. They should be chosen small, compared to the 
detector intrinsic resolution, but not too small, as the computational 
overhead in evaluating the spectral models is roughly proportional to the 
number of energy ranges. The ranges need not be evenly spaced, and because
the model evaluation is supposed to use the R(j,i) as the AVERAGE response
over the energy bin, it might prove more accurate to use the edges in the 
detector response as some of the bounds.

    For convenience the other bounds should be spaced by submultiples of
2, i.e. spacings of 2 keV, 1 keV, 0.25 keV, 0.03125 keV, etc. This is
not a strict requirement, however this makes it easier to combine fits
of multiple detectors with differing amounts of resolution. 

    The definition of the R(j,i) is such that it should include ALL
the spectrally dependent information, including telescope vignetting,
correction for scattering outside the integration pixel, etc. The
quantity of R(j,i) summed over all the PHA channels (summed over j) is
the probability that an incident photon in the ith range was detected at 
all, i.e. the quantum efficiency of the experiment in the ith channel. 
If S(i) is the incident number of photons cm**-2 s**-1 and A is the total
effective area of the instrument, independent of spectral corrections, 
then
 	C = 0.
 	do I=1,number_energy_ranges
	    C=S(i)*R(j,i)
	end do
	C=C*A 
is the expected count rate (counts per second) in the jth PHA channel. 

		***** RSP file format (SF) ****** 

    Each data file has associated with it a response file to convert
incident model spectra to the expected number of counts.  This response
file contains all the energy dependent information about the detector
response.  The response files (default extension .RSP) are SF format
files (see the associated documentation) with file type `XSPEC rspnse'. 
The `SF history' package should contain ASCII records with all the
information about what went into the creation of the response (e.g.
creation date, special fudge factors, etc.). After that there are a
variety of packages, which should be in the following order:
 	'detect info ' - describes the detector
 	optional detector dependent packages, not used by XSPEC
 	optional method packages, containing numerical information 
		used in creating the response, not used by XSPEC
 	'grouping    ' - A grouping card, if the response has been 
			 compressed. (NB. the current release of XSPEC
			 does NOT support compressed responses)
			 (see DATA.DOC for a description of the grouping 
			 card).
 	'chanel bound' - An approximate representation of the energy 
			 range that a single channel corresponds to.
			 creating the response, not used by XSPEC
	'response    ' - The actual information for the response.
Additional packages can be inserted in any order.  They will be ignored
by XSPEC. 

    The 'detect info ' package has a 100 byte header record organized as 
follows:
 	DETID	c16	- A character string containing the detector ID
 	NBIN	i4	- The number of entries after compression
 	NCHAN	i4	- The number of PHA channels for the detector 
			  before grouping (if NBIN is not equal to NCHAN 
			  then there must be a grouping package)
	RSPAREA	r4	- The total effective area of the RESPONSE. N.B.
			  In the discussion above, the area is to be
			  considered the response to a flux of photons 
			  per cm**2. Thus this number should be 1.0. Other
			  systems might scale the response differently,
			  in which case the number here will be non unity. 
			  Effectivly, the response is for a fictitious 
			  detector with RSPAREA as its area.  This is NOT 
			  the same number as the AREA of any PHA file.
 	NRANGE	i4	- The number of (contiguous) energy ranges over 
			  which there is significant response.
 	E0	r4	- The lower limit of the first energy range.
 	SPARE	44	- Reserved for future expansion (should be set to 0)

    The 'chanel bound' package is NBIN*2 values which give the
approximate boundaries in keV that the channel corresponds to.  All the
information is included in a header which is dimensioned real*4
EBOUND(2,NBIN) where EBOUND(1,I) is the lower limit of the Ith bin and
EBOUND(2,I) is the upper limit.  Note that due to the inexact nature of
X-ray detectors, these values are only illustrative of where the photons
that produce the observed counts may be coming from. 

    The `response' package contains all the R(i,j) values.  Because
this matrix can be very sparse, only the significant values are stored. 
The package has NRANGE*3 subsidiary records, of variable length, a set
of three for each energy range.  The first contains a record of
information for that range of 12 bytes:
	E	r4	- The upper energy of the current energy range. 
			  (The lower energy is the value of E in the 
			  previous record, or E0 from the `detect info'
 			  package for the first record).
	NGROUP	i4	- The total number of groups of contiguous bins 
			  with response.
	NENTRY	i4	- The total number of R(i,j) values written on 
			  this record. The second record consists of: 
	BINRNG	i4(2,NGROUP)- The lower and upper bin numbers for each 
			      group. The third and final record for the 
			      set is 
	INRESP	i4(NENTRY)  - The actual R(i,j) values. Note that if an 
			      energy range has no non-zero response then 
			      both NGROUP and NENTRY should be zero. Also 
			      NENTRY is equal to the sum over all the 
			      groups of BINRNG(2,i) - BINRNG(1,i) + 1.  
			      However, even if NGROUP and NENTRY are zero, 
			      three records are still in the package. The 
			      values of the second and third should be 
			      ignored in this case.