xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec
 xspec                                                       xspec
 xspec   Detector specific information in PHA/RSP files      xspec
 xspec                                                       xspec
 xspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspecxspec

    Such information is contained in an SF package that follows the 
`file info' package in PHA files and the `detect info' package in RSP 
files. The package name is unique for a given detector.  All EXOSAT 
detectors have "EXOSAT" as the first six characters. 

ME detectors
    For ME detectors the package name is `EXOSAT ME'.  The package
    consists of a 108 byte header and 1 to 16 100 byte auxiliary records. 
    The header is:
	GAS	c2	"AR" if Argon, "XE" if Xenon and "AX" if both
			Argon and Xenon data are included.
	INCRES	L1	If true, then resolution information is 
			contained in the aux. records.
	INCGN	L1	If true, the corrected gain information is
			included in the aux. records.
	REVIS	i4	A flag indicating the revision level (SHF key)
			of the information used to produce this file
			(e.g. detector areas, orientations, FWHM, or
			spectral calibration info if this package is
			found in an RSP file).
	SHF	i4	SHF key of observation date.
	H1ANG	r4	Offset angle of the first half (average if
			the data includes multiple offsets).
	H2ANG	r4	Offset angle of the second half.
	INCDET	L1(8)	If true, then the Ith detector is included
			in the accumulation.
	SYSTEM	i4	Coordinate system (see 'source info' package)
	SCXAXIS	r8(3)	Space craft X-axis
	SCYAXIS	r8(3)	Space craft Y-axis
	SPARE	20	Future expansion.
    Each included detector will have one auxiliary record (two if both 
    Argon and Xenon data are included):
	DETNUM	i4	The detector number (from 1-8 for AR, 9-16 XE).
	COLRSP	r4	The collimator response.
	ASSAR	r4	The assumed on-axis area.  Thus the contri-
			bution of this detector to the area in the
			`obs info' package is ASSAR*COLRSP.  During the
			life of the instrument this ASSUMED number
			should probably remain constant.  If updates
			are found in the process of the calibration
			they should be included in the program calcula-
			ting the response file (as they are probably
			small).  (When this package is found in an
			RSP file it is the value used in scaling the
			rsponse.  If the current cal knows that the
			area is TRAREA, then all the responses have
			been multiplied by an
			additional correction factor TRAREA/ASSAR.)
	AG	r4	The analogue gain setting.
	GCOEF	r4(4)	Gain coefficients.
	RESOL	r4(8)	Resolution coefficients.
	USEDRSPAREA r4
	DETINTT r4	integration time
	SPARE	28	Future expansion
GSPC detector
    The package `EXOSAT GSPC' describes the GS status. It has a 
    120 byte header.
	BLWSTART	i2	Burstlength window start
	BLWEND		i2	Burstlength window end
	NOMINALGAIN	r4	Nominal gain setting
	GAINCOR		r4	Gain correction factor
	USELINE		l1(4)	Flag for using up to 4 lines to 
				calculate gain correction factor, 
				currently not possible, set to false
	USEGAINCOR	l1	Flag for using GAINCOR
	LINECHAN	i4(4)	Channel numbers of up to 4 lines
				currently set to 0
	REVIS, SHF, SYSTEM, SCXAXIS, SCYAXIS, COLRSP, ASSAR,
	and USEDRSPAREA		as for ME
	flgcolrsp	i2	Flag for collimator response being
				in pha file
	SPARE		13	Future expansion
LE detectors
    The package 'EXOSAT LE' has a 120 byte header.
	LEID		i2	Telescope id (1 for LE1, 2 for LE2)
	DET		c3	CMA or PSD
	FILTER		i2	Filter number 	2: ppl
						3: 4000 LEX
						6: alp
						7: 3000 LEX
						8: bor
	REVIS, SHF, SYSTEM, SCXAXIS, SCYAXIS as for ME and GSPC
	NOPIX		i2	Number of pixels in x
	NOPIY		i2	Number of pixels in y
	PIXSIZE		i2	Pixel size in x (arcsec)
	PIYSIZE		i2	Pixel size in y (arcsec)
	XPIX		r4	Source centroid pixels (abscissa)
	YXPIX		r4	Source centroid pixels (ordinate)
	STTIMEYY, STTIMEDDD, STTIMEHH, STTIMEMM, STTIMESS
			i2	Start time in year,day,hour,min,sec
	ENDTIMEYY, ENDTIMEDDD, ENDTIMEHH, ENDTIMEMM, ENDTIMESS
			i2	End time in year,day,hour,min,sec
	BGBOXNO		i2	No of background boxes
	SPARE		17	Future expansion