## Slide 1
NICER Analysis and Calibration Craig Markwardt (NASA/GSFC) & NICER Team
GSFC
NICER/IXPE Workshop July/August 2024

## Slide 2: Summary
Motivation
`nicerl2’ and how to use it
Basic calibration recommendations
Understanding basic screening

## Slide 3: Motivation
Why are we here? ASTROPHYSICS!
NICER is non-imaging, but has high throughput and good spectral resolution
Astrophysics Topic | Dimension | Technique | NICER?
Energy Dissipation | Energy | Spectroscopy | ✅
Geometry | Image | Imaging | ❌
“Physics” | Time | Light curve / timing | ✅

## Slide 4: NICER Workflow Overview
NICER Data (from archive)
nicerl2 (calibration, screening)
Spectrum Responses & Bkg
Light Curve
nicerl3-spect (extract, responses, bkg, syserr)
nicerl3-lc (extract)
Level 1
Level 2
Level 3
This Presentation

## Slide 5: NICER Tools Come from HEASARC
The High Energy Astrophysics Science Archive Research Center (HEASARC) distributes NICER’s
  Software
  Calibration products
  Data
  Documentation https://heasarc.gsfc.nasa.gov/docs/nicer/

## Slide 6: Ways to Get Help
Consult on-line NICER documentation for analysis issues
  Software guide overview
  Analysis “Threads” - procedures for common tasks
  Analysis tips for specific known problems or issues you may encounter
Send questions to the NICER helpdesk: https://heasarc.gsfc.nasa.gov/cgi-bin/Feedback

## Slide 7: Introducing “nicerl2”
nicerl2 is the standard NICER pipeline preparation script. It has three main duties
  Apply energy scale and other calibration
  Construct filter file (MKF file)
  Apply screening to remove “bad” times and misbehaving detectors
  Results:
    Cleaned event list, called the “cl” file
    Event list has Good Time Intervals or GTI
    Event list has NICER FPM Selection Information or FPM_SEL

## Slide 8: Before Running nicerl2
If this is your first time with NICER data, you will have to set up the environment variable GEOMAG_PATH and put it in your start-up file
Make sure you have up-to-date geomagnetic quantities by running nigeodown
Do this before starting any new project, or with very newly observed data
Download data from archive
  We have a Thread that describes how to do this

## Slide 9: How to Use ”nicerl2”
From the command line nicerl2 /path/to/1234567890 clobber=YES
This may take some time
  clobber=YES will allow the task to overwrite old files
Results
  1234567890/auxil/ni1234567890.mkf
    “Filter” or “MKF” file
  1234567890/xti/event_cl/ni1234567890_0mpu7_cl.evt
    “cl” or cleaned event file
  1234567890/xti/event_cl/ni1234567890_0mpu7_ufa.evt
    “ufa” or lightly cleaned event file
See example notebook NICER_data_reduction
Path to Observation
DEMO

## Slide 10: Basic Calibration Recommendations
When starting a new project, always reprocess data with newest software and calibration, and update your geomagnetic quantities
  The NICER pipeline often does not use the newest releases
  Archival data may indicate “zero exposure” but you may recover some data
  Be prepared for changes due to optical light leak
Ask for help at the NICER website

## Slide 11: Calibration Done by “nicerl2”
nicerl2 applies a gain correction to all events so that all detectors are on the same energy scale
  Column name PI in event file
    ”Energy” = (10 eV) x PI
  Also PI_FAST which is a secondary pulse height channel (not normally used for science)
  Accurate to ~10 eV in 0.3-7 keV range
Time correction based on known time offsets
  Accurate to 50 nanoseconds
Identifying correlated noise/undershoot ringing events

## Slide 12: Screening by “nicerl2”
Temporal screening
  Orbit: SAA (saafilt), cutoff rigidity (cor_range)
  Pointing: tracking target (trackfilt), on target (angdist), star tracker tracking (st_valid), earth elevation (elv), bright earth avoidance (br_earth)
  Detector behavior: undershoot resets (underonly_range), overshoot resets (overonly_range), threshold setting (threshfilter)
Per-detector screening
  FPM: Undershoots (underonlyscr), overshoots (overonlyscr), noise peak (noise25scr), extended noise peak (noiseextscr), noise ringing (kee_noisering)
  MPU: “shredded GTIs” (mpugtiscr), “round robin” effect (roundrobbinscr), high data rate losses (lowmemscr)

## Slide 13: What are Undershoots?
Silicon drift detector anode gradually charges due to various effects
“Undershoot” is due to discharge/reset events
  Completely normal
Optical photon
X-ray photon
Leakage Current
SDD
Anode
Cathode
Charge
Reset Threshold
Time
X-ray or charged particle
Reset
Reset

## Slide 14: Cause and Effect of Undershoots
Typical causes of undershoots are
  Optical light!
    This is a special problem after the light leak event of May 2023
  X-rays, cosmic rays, leakage current (minor)
Undershoots cause increased noise and shift of energy scale
Desirable range for undershoots
  0-500 ct/s/FPM is calibrated range
  0-100 ct/s/FPM is desirable
  You can adjust filtering with underonly_range=0-500
See example notebook MKF

## Slide 15: What are Overshoots?
If an X-ray or charged particle deposits more than ~20 keV in a detector, we get an overshoot
  Basically “too much energy to measure”
Anode
SDD
Cathode
Charged Particle
X-ray photon

## Slide 16: Cause and Effect of Overshoots
Typical causes of overshoots are
  High energy charged particles which deposit ~200 keV of energy in a detector as they pass through
  High energy X-rays, low energy charges (minor)
Overshoots are a good diagnostic for a “dirty” or “clean” background environment
Desirable range for overshoots
  0-30 ct/s/FPM is calibrated range
  0-100 ct/s/FPM is typical SAA range
  0-1000 ct/s/FPM is typical max range
  You can adjust filtering with overonly_range=0-100

## Slide 17: Special Topic: Light Leak
Starting in May 2023, NICER experiences the effects of damage and light leak
Several leaks found, including worst one:

## Slide 18: Light Leak Effects
The impacts of the light leak during orbit day are
  Much higher data rate
    Increased chances of lost or “shredded” data
  Much higher undershoots
    Increased chances distortion of energy scale
  Low-energy detection threshold is now adjusted at every orbit day and night transition
    Affects analysis
  Still very good chances of high-quality data!
During orbit night, expect continued excellent performance
Current software handles most of these conditions

## Slide 19: How to Deal With Light Leak
By default, nicerl2 only lets through “night” threshold level (night-only data)
You need to re-screen your data, by hand, to get a separate set of “day” data nicerl2 1234567890 threshfilter=DAY clobber=YES
And then proceed with this data as normal
See example notebook Day_Versus_Night_Example

## Slide 20: What is Next?
Once you have a cleaned event list (“Level 2”) you are ready to make spectra and light curves
Spectrum Responses & Bkg
Light Curve
nicerl3-spect (extract, responses, bkg, syserr)
nicerl3-lc (extract)
Level 2
Level 3
Cleaned Event Data