## Slide 1: XRISM/Resolve data (a whirlwind tour)
February 22, 2023
F. Scott Porter
XRISM/Resolve Instrument Scientist
NASA/GSFC

## Slide 2
An x-ray calorimeter is a thermal measurement of the photon energy
High resolution non-dispersive spectrometer
linear detectors: large bandpass
Must operate at low temperatures for high resolution
IR/microwave

## Slide 3: Resolve detector system
Detector Array
Focal Plane Assembly
Anti-coincidence detector

## Slide 4: X-ray signal path
bias
XBOX
8 Mb/s
Pulse Shape Processor
Event list:
PH (det units)
Event time
Risetime
Grading
Pile-up
etc
Ground station
Quick
look
Pre-pipeline (fff)
Pipeline
Observer data
20 kb/s

## Slide 5: Pulse height processing and event grading
Want to measure x-ray energy
Use all available information
  Optimal estimator
    Signal/noise in all freq bins
What do you do with pile-up?
Two kinds of pileup
  Effects the pulse thermally
  Only effects the pulse processing
Event grades:
  High Resolution  full record
  Mid Resolution  ¼ record
  Low Resolution  Simple PH
  Secondaries (only mid and low)
Primary
Secondary

## Slide 6: Event grades
Full event grading matrix for Resolve
Ishisaki et al. (2018)

## Slide 7: Branching ratio

## Slide 8: Grading performance
Both Hp and Mp must meet energy resolution requirement of 7eV
Low res and secondaries are degraded
Example from ground data:
At 6 keV:
Hires: 4.2 eV
Midres: 4.5 eV
Lowres: 14.6 eV

## Slide 9: Calibration
Put physical units on instrument data
Parameterize model of the instrument response
Correct instrument non-linearities
Examples:
  Line spread function and redistribution (inputs to rmf)
  Spectrometer Energy Scale and reconstruction
  Throughput (i.e. effective area)

## Slide 10: Spectral redistribution
Core line shape: dominated by detector intrinsic noise and system noise
Broadband redistribution: dominated by detector material properties.
To measure: Monochrometers, modeled fluorescent lines, EBIT measurements

## Slide 11: Core line shape
Deviates from a gaussian instrumental function at the 1% level

## Slide 12: Core line shape across the band pass
Energy resolution scales with Energy
Some systematic differences between monochrometer and fluorescent measurements: incomplete line shape knowledge

## Slide 13: Energy Scale measurement
One of 3 sets of measurements to span bandpass
Precision dominated by fluorescent line models

## Slide 14: Low energy measurements with EBIT
EBIT results for Neon
Energy scale error = +0.41 eV, Energy resolution = 3.83 eV (composite 35 pixels)

## Slide 15: Summary of EBIT results
Target species | Injected gas | Lines fit | Nominal energy | Energy resolution | Energy scale error
Nitrogen | N2 | He-like | 424 eV | 4.05 eV* | +0.75 eV
Oxygen | CO2 | He-like | 565 eV | 3.81 eV | +0.62 eV
Fluorine | C3F6 | He-like | 732 eV | 3.81 eV | +0.59 eV
Neon | Ne | He-like and lower charge states | 905 eV | 3.83 eV | +0.41 eV
Silicon | DMTSiloxane | He-like and lower charge states | 1860 eV | 3.85 eV | +0.09 eV
Sulfur | SF6 | He-like and lower charge states | 2445 eV | 4.20 eV | +0.02 eV
Fluorescent line energy scales meet requirements
Some systematic errors which can be corrected using EBIT measurements.

## Slide 16: Energy scales (cont’d)
Energy Scale is non-linear and varies with temperature
Need to reconstruct vs time on-orbit using a fiducial

## Slide 17: Energy scale reconstruction
XRISM has two fiducials to track detector gain vs time:
Calibration pixel with internal 55-Fe source (5.9 keV), always on
Modulated x-ray source: flood source for all pixels, but well defined time
Cal pixel
Hitomi on orbit

## Slide 18: Energy scale reconstruction
Long term (downward) drift of ~1.2 eV
0.75 eV orbital variation
Gain tracking function
Hitomi on orbit

## Slide 19: Anti-coincidence detector energy scale
Low voltage ionization detector behind the main detector array
Dual independent readouts for redundancy
Energy scale is very linear
Use same RTS measurements, use the fact that the main array is partially transparent

## Slide 20: Summary
XRISM/Resolve instrument consists of thermal detectors
Each pixel is an independent spectrometer
Requires extensive ground calibration and in-flight verification
The ground calibration is complete (still analyzing)